## Slide 1: Autocad 101
Drawing Set-up & Introduction to CADD

## Slide 2: Open AutoCAD Architecture.
1. Open the start menu, choose ALL PROGRAMS
2. Find the folder labeled AUTODESK.
3. Open the folder labeled AUTOCAD ARCHITECTURE 2016 – ENGLISH.
4. Open AUTOCAD ARCHITECTURE 2016 – ENGLISH.
1
2
3
4

## Slide 3: Set-up a metric drawing.
Be patient, it may take a moment to load.
Choose template.
Scroll down to find acadiso.dwt.
Select it.

## Slide 4: AutoCAD TIP #1
To scroll in and out, use the ‘wheelie-ball’ on your mouse. Try that now.
To move around the screen, push down the ‘wheelie-ball’ and move your mouse around the screen.

## Slide 5: AutoCAD TIP #2
When you type a command, it will show up in the COMMAND BAR.
Watch the command bar for prompts or instructions throughout your drawing(s).

## Slide 6: Set-up layers.
Type in LAYER  hit ENTER
Find the NEW LAYER button  click it.
Create the following layers. Be sure that you are using all capital letters.
Note: watch for changes in each column.

## Slide 7: AutoCAD TIP #3
Tabs are found at the top of your screen.
Each tab categorizes various commands in organized groups.
Click on various tabs to explore AutoCAD.

## Slide 8: Set-up text.
Click on the ANNOTATE tab.
Find the small arrow in the bottom right corner of the TEXT block  click it.
Choose STANDARD, in left box  then click NEW on the right side.
Create the following TEXT STYLES (all capitals):
TITLEBLOCK HT: 4.0mm
DIMENSION HT: 2.0mm
ISO30 HT: 2.0mm OBLIQUE ANGLE: 30.0
ISO330 HT: 2.0mm OBLIQUE ANGLE: 330.0
Click APPLY  click CANCEL.

## Slide 9: Set-up dimension.
Click on the ANNOTATE tab.
Find the box in the DIMENSION block  click it to show a drop down menu.
Click MANAGE DIMENSION STYLE.
Choose ISO-25, in left box  then click NEW on the right side.
On the next slide, follow along and complete each of the windows. Be sure that you do not miss anything.

## Slide 10: Dimension settings.
Note: Follow the next few slides. Check each window VERY carefully for any changes. Small discrepancies can make a huge difference in the appearance of your dimensions.
If you would like a PDF copy of the dimension set-up, it can be found on selkirkdrafting.weebly.com under Videos & Resources.
Name your new dimension style SELKIRK BASIC
Start with: ISO-25
ISO-25

## Slide 13: Be sure to save the drawing to your STUDENT NUMBER directory (on the server). DO NOT SAVE TO MY DOCUMENTS!
SAVE!

## Slide 14: Common AutoCAD commands to know.
SHORTCUT COMMAND
L LINE
DT DYNAMIC TEXT
C CIRCLE
M MOVE
RO ROTATE
A ARC
CO COPY
O OFFSET
SHORTCUT COMMAND
E ERASE
EX EXTEND
F FILLET
H HATCH
MA MATCH PROPERTIES
PROP PROPERTIES MENU
F3 OBJECT SNAP ON/OFF
F8 ORTHOGRAPHIC ON/OFF

## Slide 15: AutoCAD TIP #4
If you need to change any item (line, circle, dimension), you will find it in the PROPERTIES MENU.
If you do not see the properties menu – type, PROP (followed by ENTER) to make it appear.

## Slide 16: If AutoCAD shuts down unexpectedly (crashes) and it asks you to save, DO NOT SAVE! You could lose your entire drawing.
SAVE OFTEN

## Slide 17: How to submit an AutoCAD file.

## Slide 18: AutoCAD Rubric